## Slide 1: Blowfish Encryption Using UART on FPGA
Hardware Implementation • UART Communication • RTL Architecture

## Slide 2: Overview
  FPGA implements Blowfish block cipher
  UART used for key/plaintext input and ciphertext output
  Hardware FSM manages flow automatically
  High‑speed, secure hardware encryption

## Slide 3: Blowfish Algorithm
  64-bit block cipher with 16 Feistel rounds
  Uses P-array (18 × 32-bit)
  Four S-boxes (1024 × 32-bit total)
  F-function: S-box lookups + addition + XOR

## Slide 4: Feistel Encryption Flow
  Split 64‑bit input → L (32 bits) and R (32 bits)
  For each of 16 rounds:
  • L = L XOR P[i]
  • R = R XOR F(L)
  • Swap L and R
  Swap L and R for final round
  Final XOR with P[16] and P[17]

## Slide 5: UART Interface
  FPGA receives 16 bytes:
  • 8 bytes → Key
  • 8 bytes → Plaintext
  After encryption, FPGA sends 8‑byte ciphertext
  Baud rate e.g. 9600/115200

## Slide 6: FPGA Hardware Architecture
  UART RX → RX FIFO → Blowfish Core
  FSM triggers when FIFO full
  Key + plaintext assembled in registers
  Ciphertext written to TX FIFO → UART TX

## Slide 7: System FSM Stages
  1. IDLE – Wait for FIFO full
  2. READ – Pop 16 bytes (key + plaintext)
  3. EXPAND (optional) – Expand key
  4. ENCRYPT – Run Blowfish rounds
  5. SEND – Stream ciphertext bytes over UART

## Slide 8: Benefits of FPGA Implementation
  Parallel S‑box access → faster than software
  Deterministic timing
  Secure on‑chip execution
  Simple PC interface via UART

## Slide 9: Applications
  IoT hardware security
  Encrypted communication modules
  Hardware crypto accelerators
  Real‑time embedded encryption

## Slide 10
Github Repo:
https://github.com/Mohit14036/FPGA_Project_course.git

## Slide 11
Latency: 216ns
18 cycles for first output and 12ns clock period

## Slide 12
Utilization